T-300B

Landscape Garden Speaker

Features

- Built-in 100v/70v transformer

- Landscape rock shaped garden loudspeaker

- IP66 waterproof level

- 6.5”+1.5” two ways driver

- Power taps at 7.5W & 15W @100V

- Organic resin material

- Heavy damage proof finish

Description

The T-300B is a landscape garden speaker built-in 70v/100v transformer. The 70v/100v transformer technique reduces line losses on longer distance and allows easy parallel connection of multiple loudspeakers.

The built-in 6.5” +1.5” two way speaker drivers are designed of wide frequency response 120-15kHz, the multiple power taps of 7.5W & 15W could meet different applications varies from room size and ambient noise surroundings.

The fiber-glass enclosure is of sandy brown color and of weatherproof and heavy damage proof finish. Easy and secure wall mount installation in outdoor area.

It is ideal choice for park, playground, swimming pool and garden etc outdoor applications where background music and paging is needed. It is designed of IPx6 waterproof level, so it could be directly exposed to outdoor severe environment, the organic resin material is strong resistant to cold, snow, ice, high temp and sunshine.

Specification

| Model | T-300B |
| --- | --- |
| Power Taps @100V | 7.5W, 15W |
| Power Taps @70V | 3.8W, 7.5W |
| Impedance | Black: Com White: 800Ω Green: 400Ω |
| SPL(1W/1M) | 95dB |
| Max. SPL (Rated W/1M) | 109dB |
| Frequency Response (-10dB) | 120-15KHz |
| Finish | Organic resin |
| Speaker Driver | 6.5"+1.5" |
| IP Rate | IP x 6 |
| Cutout Size | 295mm |
| Dimensions(mm) | H:265 |
| Weight | 4.3Kg |

Website: www.itc-pa.com.cn; Mail: info@itc-pa.com.cn

Page 2 of 1

T-300B

Landscape Garden Speaker

Appearance:

Direction Diagram:

Frequency Response：

Website: www.itc-pa.com.cn; Mail: info@itc-pa.com.cn

Page 2 of 2