High-end Entertainment Loudspeaker

TS-815

Product Description

* Adopt the bass neodymium speaker unit 15 inch and one 1.7 inch compression

neodymium tweeter

* The box body is made by 15mm birch. Light quality, wear-resistant paint treatment,

inner side pasted with dustproof net cotton

* Precisely designed to optimize power divider IF response and expressive vocal parts

* A plurality of screw holes lifting, a diameter of 35 mm pole sockets, a variety of

Installation

The scope of application

Used together with TS professional stereo amplifier and sound effect processor system,

to form a set of high-end entertainment amplification system with perfect sound and

outstanding vocal performance. It's suitable the music bar, KTV room, high-grade room,

hall, etc. If used together with subwoofer, it can be used as high-performance satellites.

Specifications

| Model | TS-815 |
| --- | --- |
| Impedance | 8Ω |
| Frequency | 40Hz-20KHz |
| Rated Power | 500W |
| Sensitivity | 100dB/W/M |
| Angle of coverage | (H)90°(V)70° |
| Treble | 1.7 "compression tweeter x 1 |
| Bass | 15 "bass x 1 |
| Dimensions | 680 x 430 x 430 mm |
| Weight | 22Kg |