Mixer Pre- Amplifier (8 Inputs & 2 Outputs)

T-8S02

Connections

Features

* Standard machine cabinet type 1 U height design, black aluminuim oxide drawbench panel.

* With 8 inputs interface which can be converted independently, adopting European style terminals.

* Double bus design with main channel/ accessory channel output selector.

* One independent accessory input interface, adopting European style terminals.

* Multi-channel input audio mixed into public output bus directly, adopting balanced input and output.

* With line and mic selective switch for each channel, output to AUX connector.

* Each input channel can be gain controlled, input with low cut filter.

* Knob input level can be controlled independently in each channel.

* With phantom power switch power supplied to condenser microphone.

* Knob is independently controlled in main output and auxiliary output.

* Main output is equipped with voltage limit which is with by-pass switch, threshold value and ratio value and can be controlled.

* With LED output indicator on panel, and with earphone output function.

Specifications

| Model | T-8S02 |
| --- | --- |
| Input Sensitivity/Impedance |  |
| 1-8MIC/ Line | 0.25mV/5KΩ balanced, ±7.75V/5KΩ balanced |
| AUX1 RCA In | ±0.775V/20KΩ unbalanced |
| Output Level/Impedance |  |
| Master 1, -2 | +4 dBμ/440Ω balance (MAX:±7.75V) |
| Main Output MIC Pad | -50 dB |
| Low Cut | 18 dB/octave at 100 Hz |
| Frequency Response |  |
| Less Than | -1dB(20Hz~20KHz) |
| S/N Ratio |  |
| MIC | More than 60dB |
| Line | More than 75dB |
| THD |  |
| MIC | Less than 0.05% |
| Line | More than 0.03% |
| Cross-talk |  |
| MIC | More than 60dB |
| Line | More than 75dB |
| LIMITER/COMPRESSOR |  |
| Threshold Adj. Range | -20 dB to +20 dB |
| Ratio Adj. Range | 0 to 100% |
| LED Bar Graph | -18, -12, -6, -3, 0, +3, +6, +12VU (0 VU = +4 dB) Average or Peak reading |
| Power Consumption Power | 20W |
| Power Supply | ~110V/60Hz or ~230V/50Hz |
| Dimensions | 484x190x44mm |
| Weight | 3.9Kg |