2-Channel Class-D Power Amplifier

T-2D120

T-2D240

T-2D350

T-2D500

Rear Panel

Connections

Descriptions

The range of one channel power amplifier is Class-D series. From one hand, switch power

technology with APFC (Active power factor correction), had enhanced the efficiency up to 85%.

From another hand, this amplifier is also preferable for much more heat generation of less

than 55 degrees even at severe working conditions, thus this benefits are not only good for extension of life span.

The amplifiers are designed to be both tabletop and rack mount in 1.5U height. The output

power of this series is 120W, 240W, 350W and 500W. On the real, there is one line 100V output to connect with speaker. A line input by phoenix connector for remote control and status monitor. Extensive protection includes high temp, overload and short-circuit.

Features

* Built-in active filters band pass signal to effectively filter out useless audio signal.

* 2 channel balanced line inputs, 2-channel 2 x 120W/240W/350W/500W power output.

* Independent volume control.

* LED indicator includes signal, peak, protection, power supply signal.

* With amplifier monitor output, standby control and standby cascade port.

* With DC24V input, with wide voltage range protection (21.6 ~ 26.5Vdc), to avoid damage to equipment in case of long-term feed failure from backup battery or voltage is too high.

* AC230V 50Hz power supply.

* Output: 100V.

* Electrical isolation for device, signal input and output, it is 3C, UL, IEC60065 certification

standards.

* Built-in short circuit, overload, overheating protection.

Specifications

| Model | T-2D120 | T-2D240 | T-2D350, | T-2D500 |
| --- | --- | --- | --- | --- |
| Rated Power Output | 2 x120W, | 2 x240W | 2 x350W | 2 x500W |
| Speaker Output | 100V |
| Input Sensitivity & Impedance | ±385mV/20KΩ,balanced H5.08 European connector input |
| Overload Electromotive Force | ＞11dB, balanced H5.08 European connector input |
| Frequency Response | 80Hz~18KHz(+1dB, -3 dB) |
| S/N Ratio | ≥85dB |
| THD | ≤0.5% at 1KHz, 1/3 rated power |
| Controls | Remote volume control, power control, standby control and status monitor (phoenix connector) |
| Indicators | signal, peak, protection, power |
| Protection | high temp, speaker, DC output ,overload and short-circuit |
| Cooling | Forced cooling (half speed control start up 50℃ ; full speed control start up 70℃ ) |
| Power Consumption | 300W | 550W | 800W | 1550W |
| Power Supply | ~230V 50Hz(can be customized to be AC110V 60Hz) DC24V( 24V DC battery standby) |
| Dimensions | 484 x 440 x 66mm |
| Weight | 8.1Kg | 8.2Kg | 8.4 Kg | 8.5Kg |