Mixer Amplifier (Phone Jack MIC Input)

T-35M/T-60M

Rear Panel

Feature

*  3 MIC inputs, 2 AUX inputs

*  3 MIC volume control, 2 AUX volume control

*  With priority, MIC1 input is prior to other audio input

*  There is a separate treble and bass adjustment knob

*  One MIC2 / AUX1 selector switch, one MIC3 / AUX2 selector switch

*  Two types of power output: 4 ohms constant resistance, 8 ohms output and constant voltage 70V, 100V output

*  Single-channel rated power 35W / 60W output

Specifications

| Model | T-35M | T-60M |
| --- | --- | --- |
| Rated Power Output | 35W | 60W |
| Speaker Outputs | 70V, 100V & 4~8Ω |
| Input Sensitivity & Impedance | MIC 1, 2, 3: 5mV/600Ω, Unbalanced phone jack input |
|  | MIC2: 775mV/10KΩ, Unbalanced phone jack input |
|  | AUX2: 350mV/10KΩ, Unbalanced RCA input |
| Output Sensitivity & Impedance | MIX OUT: 1V/470Ω, Unbalanced RCA output |
| Tone | Bass: ±10dB at 100Hz |
|  | Treble: ±10dB at 10KHz |
| Frequency Response | 50Hz~16KHz(+1dB, -3dB) |
| S/N Ratio | MIC 1, 2, 3: 66dB, AUX 1, 2: 80dB |
| THD | Less than 0.5% at 1KHz, 1/3 rated power |
| Crosstalk | ≤50dB |
| Cooling | Fan automatically start up when temp reaches 55℃ |
| Protection | High temp, overload & short-circuit |
| Power Supply | ~110V/60Hz or ~230V/50Hz |
| Power Consumption | 60W | 100W |
| Weight | 3Kg | 3.5Kg |
| Dimensions | 484 x 335x88mm |
| Finish | Panel: steel plate, black Case: steel plate, black |